## Slide 1: Simulation of Real Time Traffic and Black Hole Attack in NS-3
Group : CS-14 Deepak Bulani 20153026 Gaurav Agarwal 20154097 Bonthu Harsha Vardhan Reddy 20154148 Avichal Verma 20154085 Amit Ranjan 20154101 Under the guidance of Dr. Dinesh Singh MNNIT Allahabad May 3rd 2018

## Slide 2: Outline Of The Project
Mobile Ad Hoc Networks (MANET)
Integration of SUMO with NS-3
Working Of AODV Protocol
Vulnerabilities of AODV Protocol
Black hole Attack in AODV
Conclusion
References

## Slide 3: MANET
Mobile Ad Hoc Networks are formed dynamically by an autonomous system of mobile nodes that are connected via wireless links.
No existing fixed infrastructure or centralized administration.
Each node works as a router.
Vehicular Ad Hoc Network is a special type of MANET and form a key part of Intelligent Transportation System(ITS).

## Slide 4: Network Simulator (NS-3)
NS-3 is a discrete-event network simulator whose goal is to develop a preferred, open simulation environment for networking research.
NS-3 software infrastructure encourages the development of simulation models which are sufficiently realistic to allow NS-3 to be used as a real-time network emulator, interconnected with the real world and which allows many existing real-world protocol implementations to be reused within NS-3.
A simple NS-3 script can be written in either C++ or Python language. NS-3 is built on both-C++ and Python bindings. We’re using C++ scripts in our simulation as we’re more familiar with C++

## Slide 5: Simulation of Urban Mobility (SUMO)
Simulation of Urban Mobility (SUMO) is an open source traffic simulation package .
It allows to simulate how a given traffic demand which consists of single vehicles moves through a given road network.
The simulation allows to address a large set of traffic management topics.
It is purely microscopic: each vehicle is modelled explicitly, has an own route, and moves individually through the network.
Simulations are deterministic by default but there are various options for introducing randomness.

## Slide 6: Routing Protocols in VANET

## Slide 7: AODV PROTOCOL
AODV is a packet routing protocol designed for use in mobile ad hoc networks (MANET).
This protocol establishes routes to destinations on demand and supports both unicast and multicast routing.
Networks are silent until connections are established . Network nodes that need connections broadcast a request for connection.
The remaining AODV nodes forward the message and record the node that requested a connection.
Each node maintains a routing table that contains information about reaching destination nodes.

## Slide 8: RREQ Message
B?
B?
B?
B?
B?
B?
B?
B
A
Route discovery process begins with the creation of a Route Request Packet (RREQ) . The packet contains source node’s IP address, source node’s current sequence number, destination IP address, destination sequence number.

## Slide 9: RREP Message
B
A
A
A
A
Destination node sends a Route Reply Packet (RREP). It contains IP address of source and destination, current sequence number of destination, hop count and lifetime of packet

## Slide 10
Vulnerabilities in AODV
AODV possesses some limitations due to which it is easily attacked by the external intruders.
This protocol is exposed to a variety of attacks, some of these attacks can cause a breakdown of the network connectivity, increasing the end-to-end delay, increasing the number of the loss packets, or shutting down some nodes by consuming all the energy left in their batteries.
Black hole attack is an attack in which malicious node uses its routing protocol to advertise itself for having the shortest path with minimum hops to the destination node whose data packet it wants to take away. In this way attacker node is always available to the nodes whose packets it wants to retain.

## Slide 11: Black hole Attack in AODV
Black hole is a simple but certainly effective Denial of Service attack in which a malicious node, through its routing protocol, advertises itself for having the shortest path to the destination node or to the node whose packets it wants to intercept.
It pretends to have enough of fresh routes for a certain destination. The source node assumes it to be true and the data packets are forwarded to a node which actually does not exist, causing the data packets to be lost.
When a source node wants to initiate the communication, it broadcasts a RREQ message for route discovery. As soon as the malicious node receives this RREQ packet, it immediately responds with a false RREP message to the respective node advertising itself as the destination or having the shortest path for that destination.

## Slide 12
Since the malicious node needs not to check its routing table before responding to a routing request, it is often the first one to reply compared to other nodes.
When the requesting node receives this RREP, it terminates its routing discovery process and ignores all other RREP messages coming from other nodes. Thus the data packets are sent to such a “hole” from where they are not sent anywhere and absorbed by the malicious node.
Often many nodes send RREQ simultaneously; the attacker node is still able to respond immediately with false RREP to all requesting nodes and thus easily takes access to all the routes. In this way source nodes are bluffed by malicious node which gulps a lot of network traffic to itself resulting severe loss of data.

## Slide 13
M
RREQ
RREQ
RREP
RREP
RREQ
RREQ
RREQ
S
D
A
B
C
How Black hole attack works

## Slide 14
Timeline of the Project
Study of VANET and it’s protocols
Got familiar with Network Simulator-3
Integration of SUMO with NS-3
Generated map of Civil Lines, Allahabad using OpenStreetMaps and simulated it on SUMO
Applied AODV protocol on the mobility file generated by SUMO using NS-3 and viewed it’s simulation on PyViz and NetAnim.
Studied Black hole attack and it’s effect on AODV protocol
Simulated Black hole attack in NS-3 and performed throughput analysis using Flow Monitor

## Slide 15
SUMO GUI output for Civil Lines, Allahabad Open Street Map

## Slide 16
Simulation output of “vanet-routing-compare" using SUMO mobility trace with ns3 and applying AODV routing protocol on mobile nodes.

## Slide 17
Throughput without malicious(Blackhole) node
Throughput with malicious(Blackhole) node

## Slide 18: Conclusion
In our project we simulated Black hole attack in NS3 on AODV Routing protocol. This simulation helped us gain insight in the vulnerabilities of AODV protocol and how well Black hole attack being one of the most powerful attacks on an Ad hoc network can cause a complete failure of the network by dropping all the traffic specially when the nodes are non-mobile. Additionally, we also integrated NS-3 with SUMO where we generated real time traffic whose mobility was controlled by the sumo file “mobility.tcl” and the interaction of the mobile nodes was regulated by AODV protocol.

## Slide 19: References
    AODV Protocol
Black hole attack in AODV
Network Simulator-3
    H. Moudni, M. Er-rouidi, H. Mouncif and B. El Hadadi, "Performance analysis of AODV routing protocol in MANET under the influence of routing attacks," 2016
    International Conference on Electrical and Information Technologies (ICEIT), Tangiers, 2016, pp. 536-542.
R. A. R. Mahmood and A. I. Khan, "A survey on detecting black hole attack in AODV-based mobile ad hoc networks," 2007 International Symposium on High Capacity Optical Networks and Enabling Technologies, Dubai, 2007, pp. 1-6.
Understood from : https://www.nsnam.org/documentation

## Slide 20: THANK YOU!